Achema trade fair preview (June 15-19, 2015 in Frankfurt am Main)

Precise low-pressure chromatography system for fast and safe purification of biopharmaceuticals in the GMP field

Nowhere are the requirements of precision, quality, and reproducibility as strictly regulated as in modern process chromatography. Using the Ecoprime low-pressure chromatography system developed by Lewa GmbH, batch-to-batch reproducibility in GMP manufacturing of biopharmaceuticals can be enhanced significantly and the yield of the product can be  enhanced. Unveiled by the manufacturer at the Achema trade fair this year, the system is notable within its product family for its extremely precise flow control from 0.03 to 60 liters per minute, its unrivaled dynamic flow rate range, minimal pulsation, and low holdup volume, allowing better product yield, purity, and safety during purification. As a consequence, production time and the costs of validation in the entire production cycle are able to be reduced.

The pumps installed in the systems and registered for patent approval with the servo drive from Lewa operate with the highest precision and allow high reproducibility of the adjustable parameters. Compared with other systems, a considerably higher accuracy over the entire flow rate range can also be covered with its Intellidrive technology. Each Ecoprime system therefore offers an adjustment range of 1:150 or more. Because the Ecoprime system can handle the flow rate of up to three individual conventional process systems, investment costs and valuable floor space can be reduced. It is therefore ideally suited for use in cost-intensive GMP cleanrooms.

In the previous year, a license agreement with ChromaCon AG was sought to extend the Ecoprime batch chromatography platform, which applies to the use of Capture SMB technology, among others, at pilot and GMP scale for continuous purification. This allows various process principles such as batch or multi-column chromatography, Capture SMB, and MCSGP process principles to be undertaken with the same system platform. In addition, the contract between both companies enables them to further accelerate the development of modern cost-reducing purification processes for the manufacturers of biopharmaceuticals at GMP scale.

The Lewa team can be found at Achema in Hall 8.0, Stand C62 to discuss our products and answer any specific questions you may have. The Managing Director, Stefan Glasmeyer, will also be present for the entire trade fair from June 15-19, 2015.

What: 	 			Achema

When: 			June 15-19, 2015

Where:  			Frankfurt am Main, Hall 8.0, Stand C62

Contact person:		Flemming Carlsen

Further information: 	www.lewa.de

LEWA GmbH was founded as a family company by Herbert Ott and Rudolf Schestag in 1952. Today it is the world's leading manufacturer of metering pumps and process diaphragm pumps as well as complete metering systems for process technology. The Leonberg, Germany-based company developed into an international Group within a few decades and saw further improvement in its position on the world market as part of integration into the Japanese Nikkiso Co. Ltd. in 2009. As a research and production-oriented company, LEWA develops technologies and provides solutions for the vast array of applications among its customers. The products see use primarily in the oil and gas industry in applications involving gas odorization, petrochemicals and in refineries as well as in the manufacturing of plastics, detergents and cleaning agents. Additional application areas include the chemical industry, cosmetics industry, pharmaceuticals and biotechnology, food and beverage industry and power supply utilities. LEWA currently employs around 1000 people and owns 16 subsidiaries around the world along with having representatives and sales offices in more than 80 countries.

Images:

More information for readers/viewers/interested parties:

LEWA GmbH

Ulmer Strasse 10, 71229 Leonberg, Germany

Phone: +49 7152 14-0, Fax: +49 7152 14-1303

E-mail: lewa@lewa.de

Internet: www.lewa.de

More information for press members

ABOPR Pressedienst B.V., Munich office

Leonrodstrasse 68, 80636 Munich, Germany

Phone: +49 89 500315-20, Fax: +49 89 500315-15

E-mail: pressebuero@abopr.de

Internet: www.abopr.de

Publication free of charge when citing the source, specimen copy requested

# Text boxes

Image ID: Ecoprime.jpg

Caption: With the diaphragm metering pumps of the Ecoprime chromatography system from Lewa, processes can be reproduced with the highest precision. The entire design of the product-wetted piping system is optimized for the best fluid dynamics. The assembly of the system is compliant with all pharmaceutical requirements and ensures that the system can even be placed in confined cleanroom spaces.

Source: Lewa GmbH